## Slide 1
CcpNmr Analysis Version 3
Chemical Shift Perturbation
Practical
Written by: Luca Mureddu
CCPN application developer, PhD Student
MCB, University of Leicester, Lancaster Road, Leicester, LE1 9HN, UK
t: +44 (0) 116 229 7074
e: lgm8@le.ac.uk

## Slide 2
Introduction
NMR is a very powerful technique to map the interaction between two biological partners. The peaks on the spectrum represent the correlation between the amide protons and the nitrogen connected to it (H – N) (15N – HSQC). Each peak represents an NH of each residue (except for the first residue and the prolines), the side chain of a few amino acids (Asn, Gln, His and Trp) can also give a peak.
The chemical shift (nitrogen and proton) is sensitive to the chemical environment of the two nuclei. Any chemical environment modifications of amino acids by the addition of another molecule will affect the position of the peaks in the spectrum.
The analysis and the mapping of these shifts on the protein structure will give information on the binding interface.
In this NMR practical, you will have to analyse the 15N – HSQC spectra of a 15N labelled TSTAR protein in complex with RNA and to map this interaction onto the structure of the protein.
Start CcpNmr Analysis V3 by double clicking the icon CcpNmrAnalysis.

## Slide 3
1
Open Project
1A
Drag & drop “Tstar.ccpn” into the sidebar or blank display. CcpNmr projects have an extension of type “filename.ccpn”. Find the project file Tstar.ccpn in the top directory or in AnalysisV3/data.
Select the file “Tstar.ccpn”, drag and drop into the program. The Tstar project will be loaded in a new window.
You will see five spectra, displayed as:
  Tstar-free (red)
  Tstar-0:50eq (orange)
  Tstar-1:00eq (green)
  Tstar-1:50eq (blue)
  Tstar-2:00eq (black)

## Slide 4
1
Open Project
Getting started, basic operations
Sidebar
  All spectra and peak lists are located in sidebar. Double click on an item will open the properties popup.
Display
  A display can contain multiple overlaid spectra. To show/hide a single spectrum, click on its toolbar button. See next page.
  If you close a display. You can open a new one from main menu -> view -> New Blank Display. Drag and drop into it the spectra from sidebar.
Mouse
  Pan -> Left Click and drag in display
  Zoom in/out -> Scroll wheel in display
  Context menu -> Right click
  Select a peak -> Left click on a peak symbol “X”
  Move a peak -> select first then hold Middle and drag
Shortcuts
  The program uses several shortcuts, example “CL” for copying a peak list. You will need to press the first letter on your keyboard e.g. “C”, followed by the second letter, e.g. “L” .
Fore more commands and operations: main menu -> help -> Tutorial (Beginners) or Show Shortcuts

## Slide 5
1
Open Project
1B
Toggle off all spectra apart from Tstar-2:00eq on the toolbar.
Click on the toolbar button of the first four spectra (a, b, c, d). The buttons will change colour from dark orange* (spectrum visible on the display, “toggle On”) to light yellow* (spectrum hidden on the display, “toggle Off”)
1 Click to toggle on the spectra
Toolbar buttons

## Slide 6
2
Copy Peak List
2A
Drag & drop the peak list tree item “PL:Tstar-free” into the spectrum display.
On side bar, expand the tree:
  tStar
    Spectra
      SP:Tstar-free PL:Tstar-free.2
Click to select PL:a-Tstar-free.2, drag and drop the item into the spectrum display.
Only the Free-Form Tstar has a peak list. You will need to copy this peak list to a spectrum recorded with Tstar bound to the RNA.
Drop “PL:Tstar-free.2” here

## Slide 7
2
Copy Peak List
2B
Select target Spectrum: e-200. A new popup will open, the first entry is the peak list source you want to copy; the second entry is the target spectrum, where the peak list will be copied.
Select:
Source PeakList: PL: Tstar-free
Target Spectrum: SP:Tstar-2:00eq
Press Ok

## Slide 8
2
Copy Peak List (Optional)
2C
Double Click on sidebar item “PL:Tstar-2:00eq.2 ” to change colours.
Expand the spectrum item tree SP:e-tStar-200 on side bar, like previously for the SP:free-tStar
Double click on “PL:Tstar-2:00eq.2
A new popup will open.
Select the desired colours for text labels and symbols. Close the popup.
Tip: use the same colour as the spectrum contours.
2D
Delete “PL:Tstar-2:00eq.1” from side bar. The default peak list for the spectrum Tstar-200 is empty. For simplicity delete it from side bar. Right click on the item Tstar-2:00eq.1 then click delete.
2C
2D
PL:Tstar-2:00eq.1
Right click to delete
PL:Tstar-2:00eq.2
Double click To change colours

## Slide 9
3
Move Peaks
3B
Open peak table, shortcut “LT”. Open a peak table with the shortcut ”LT” or from the main menu -> view -> Peak Table.
Select PL:e-Tstar-200.2.
On the top left corner of the peak table there is a pulldown menu, select the newly created peak list: PL:Tstar-2:00eq.2.
3C
PL:Tstar-200eq.2

## Slide 10
Move peaks manually.
Locate a single peak and zoom in using the middle mouse wheel, until it’s in the middle of the display. Hold down the left mouse button and drag to pan the spectrum.
On the peak table, double click on a row, e.g. # 10 | A.62.ILE. The spectrum display will navigate to the selected peak coordinates.
Move the mouse cursor on top the selected peak [X]: hold down the middle mouse wheel button and drag across the selected peak. The peak will start to move, when you are in the correct position, release the mouse button.
Use the shortcut “SE” to centre the peak to its extremum.
3D
3
3
Move Peaks
hold middle mouse and drag
Release
This peak list was copied from Tstar without ligand, therefore, some peak will have changed position upon titration with the ligand. You will have to find the shifted peaks and correct their position.
Double click #10

## Slide 11
3
Move Peaks
3E
3
Map the trajectory.
To map the trajectory of the peak shifts it is important to check the other spectra too.
toggle on and off manually the spectra on the toolbar to see any differences in the peak positions across the different spectra.
Useful shortcuts:
  “Tab-Tab” (press twice ⇥⇥) Displays the next spectrum and hides all others
  “Tab-A” : Displays all spectra
  “Tab-x” : Reverts displayed spectra
Repeat points 3D and 3E for all other peaks in the project. In short:
Double click on a peak table row
View the peak perturbation across the different spectra toggling on/off the spectra on the toolbar
Move the Tstar-2:00eq peak
Save the project frequently
To change the order how spectra are displayed: Middle mouse on the toolbar button and drag and drop the button to a new positon in the toolbar

## Slide 12
3
4A
4
Map Peaks
Open the Chemical Shift Mapping module, shortcut “CM”.
Once you have moved all peaks correctly, inspect the chemical shift perturbations using the Chemical Shift Mapping module.
Go to the main menu -> View ->Chemical Shift Mapping module or use the shortcut “CM”.
The Chemical Shift Mapping module includes a bar chart plot, a residue table and a settings panel.
As previously stated, each peak represents a single residue in the protein (apart from the sidechain peaks). From now on, we will refer as NmrResidue for a residue assigned to its spectrum peak. In green are plotted the NmrResidues that have moved above a threshold of 0.1 ppm; in red the others.

## Slide 13
3
4B
4
Map Peaks
Changing the default values.
Click the “gear icon” in the top left corner of the module .
Set:
Relative Contribution: H = 6.5, N = 1
Threshold line: 0.200 ppm
Leave Select Atoms as the default
You might want to change the plot colours
PDB file Path: click the folder icon and select TSTAR-KH.pdb in the pymol directory. Full path tStar.ccpn/scripts/pymol/TSTAR-KH.pdb
Click the Update All button.

## Slide 14
3
4
Map Peaks (Optional)
4C
Find the disappeared Peak.
In this protein a peak has disappeared after the titration with the ligand.
If present in the plot, double click on the residue bar 97 to navigate to the residue coordinates on the spectrum display, otherwise double click on the peak table #40 | A.97ILE.H | A.97ILE.N.
Right click and Delete the peak from the spectrum Tstar-2:00eq You can add a comment on the Comment column Chemical Shift Mapping table cell by double clicking inside the cell.
The plot will automatically refresh and mark the residue as ”missing”
4D
Export plot.
Right click in the plot in an empty space
Click Show Label Above Threshold
Click Export
On the Export popup Select Image File, then click export
Save the file

## Slide 15
3
5
PyMOL
PyMOL is a Python-enhanced molecular graphics tool. It excels at 3D visualisation of proteins, small molecules, density, surfaces. The visualisation through PyMOL of the perturbed residues on the surface's protein can be started using CcpNmr.

## Slide 16
3
5
PyMOL
5A
Click “Show on Molecular Viewer”.
By clicking the button
on the Chemical Shift mapping inside CcpnNmr Analysis, PyMol will be launched with the Tstar structure already loaded in. In Pymol two new selections will be created:
(aboveThreshold) , same colour as the bars in CcpNmr
(belowThreshold) , same colour as the bars in CcpNmr
(missing) , same colour as the bars in CcpNmr
You will be able now to analyse graphically the residues that are involved in the interaction with the ligand.
(Optional) Export image with transparent background
Copy and paste these commands on the Pymol terminal:
set ray_opaque_background, 0
png ~/Desktop/tStar.png, width=1000, dpi=300, ray=1
press enter
Find the image on your desktop
5B
Paste Here